## Slide 1: Design of processor
Made by DVIVEDI ROHAN VIPULKUMAR
2014A4PS456H

## Slide 2: Request
Please Keep the block diagram image of processor side by side while going through the presentation.

## Slide 3: Classification
The processor has only one internal Data bus
No separate BUS interface unit
No pipelining can be carried out.
Microcode execution is constant 5 pulse multicycle type.
Macrocode (code processing after there is Proper microcode to emulate an instruction set) will be of multicycle type

## Slide 4: Classification
It is a Microcoded processor as most present day processors.
It uses vertical encoded microcoding pattern each microcode is only 16 bits wide. Stored in a ROM with address bus width of 11 bits and data width of 8 bits.

## Slide 5: Classification
It is a 8 bit , single bus , multicycle , vertical micro coded processor design.

## Slide 6: Modules
Microcode counter
Microcode ROM
Microcode Decoder unit
Microcode Sequencer
Register file
ALU

## Slide 7: Microcode counter
Composed of 3 4 bit synchrous counter ICs CD4029
Signals to module :
  Preset enable for jump
  Clock to increase the address by value 1

## Slide 8: Microcode ROM
The microcode in the ROM (can & will) consists of BIOS, an interpreter for instruction execution.
There is 11 bit address and 8 bit data width
Presently Atmel AT28c16 EEPROM is being used.
There is no instruction interpreter currently present on the ROM

## Slide 9: Microcode Decoder unit
2 bytes after they are fetched from the ROM form a microcode.
Byte with even address is responsible to let some data (either from registers or immediate) to be made available for writing to some register , or to execute a jump to that corresponding address as available on internal data bus.

## Slide 10: Microcode Decoder unit
Every odd data is responsible to latch the data available on the bus to any of the register, or to the CONDBIT (conditional bit) or to the jump BIT(JUMPBIT is present in Microcode sequencer).
The CONDBIT is a single bit register which stores a 1 or 0 that can be used to make a conditional jump by setting the JUMPBIT in register.

## Slide 11: Microcode Sequencer
It is responsible for generating sequences for fetching even byte, odd byte , clocking the counter, and execution of microcode.
Presently the Microcode Sequencer uses exactly 5 pulses to different modules for execution of one instruction, There is no pipelining in the microcode execution, It can be brought by redesigning microcode sequencer

## Slide 12: Register file
It consists of 14 registers (that can be used as GPR or SPR depending on Microcode)
There are 4 registers for bus control
  1 MARH  Memory address register high
  2 MARL  Memory address register low
  3 CR  Control Register
  4 DR  Data Register
ALU registers
  1 ALU_A  A operand of ALU
  2 ALU_B  B operand of ALU
  3 - 8 Solution register cum buffer

## Slide 13: Register file
MARH,MARL , CR, ALU_A, ALU_B are the registers that can only be Latched. They can not be read to write to any other register.
Solution register cum buffers are read only registers, they can be enabled on bus but they can not be directly written.
Thus memory bus and control bus on this processor are unidirectional
Data bus is birectional.

## Slide 14: ALU
Operands are ALU_A and ALU_B
Operations that can be presently performed are bitwise binary AND, bit wise binary OR, bit wise binary EX-OR, Left rotate by 1, right rotate by 1, Flags.
Flags are
  A7 = 7th bit of ALU_A
    Can be used for signed numbers

## Slide 15: ALU flags
  > is set if ALU_A is greater than ALU_B
  < is set if ALU_A is lesser than ALU_B
  = is set if ALU_A is equal to ALU_B
  A0 is set if 0th bit of ALU_A is set
    Can be used to check if a numbers is odd or even
  Is1 This bit is set if the ALU_A is not 0
  Ab This is a very unique bit it is set if the ALU_B th bit is set on ALU_A

## Slide 16: ALU Flag Ab
This flags helps us identify a particular bit in ALU_A, It can be used for sequential multiplication, it can be used to identify a Flag on the Flag register (because the flag register in this architecture is not bit addressable)
Since to set the CONDBIT we require to have Flag register bit always at 0th position. Ab Flag is at 0th position in Flag Register.

## Slide 17: Microcode instruction format
Format 0
  XXX RRRRR XX 0 WWWWW
    Here initial 3 X bits are don’t care
    Next 5 R bits represent which register has be read on the bus (address of registers is always greater than 1)
    Next 2 XX bits are don’t care
    Next bit 0 has be always set as 0 for format 0
    Next 5 W bits are the register address to which register to write to.
    Note (address of registers is always greater than 1)

## Slide 18: Microcode Instruction Format
Format 1
  IIIIIIII YY1 WWWWW
    First 8 I bits represent Immediate value.
    Next YY bits are don’t care
    Next single bit represents the format 1
    Next 5 W bits represent the address the data has to be written to.

## Slide 19: Microcode instruction Format
Jump instructions
  They are similar to instructions
  Here unconditional jump is represented by W (write address) = 22 decimal
  Conditional jump is represented by W (write address) = 23 decimal
  Conditional bit CONDBIT can only be written and not read, its address is 21 decimal

## Slide 20: JUMP ADDRESS
Microcode instruction address width is 11 bits.
Since every instruction starts at even address only we can neglect the last bit , thus we have now only 10 bits of Microcode address bit to handle.
The Lower 8 bits of address can come from either immediate value in microcode, or from a register, while the mist significant 2 address bits only come as immediate value.

## Slide 21: JUMP address
Instruction format can be any of 0 or 1
MMMMMMMM YY L WWWWW
here M is either read address or Immediate value, L is either 0 or 1 based on presence of register address or Immediate value.
YY here represent 2 most significant bits on the jump address if and only if WWWWW is equal to 22 (unconditional jump) or 23 (conditional jump)
Bits YY have no influence on Internal data bus or any of registers.

## Slide 22: What operations can be performed ?
Pretty much any thing
  There is Hardware in ALU for AND – 7408s, OR – 7432s and EX-OR – 7486s, left rotate by 1 , right rotate by 1, and flags as mentiond.
  Flags can help in jump, Ab flag can help in jumps and multiplication, multiple Left rotate and bit masking with AND and OR can give left shift similarly right rotate can give right shift.

## Slide 23: Memory
Presently 2^16 X 8 bit memory can be directly addressed using paging on the remaining 4 bits on control register 16 pages can be established. (other than I/O read/write and MEM read/write)

## Slide 24: How to program ?
Presently There is no Instruction set programmed in the microcode. (That will be done later).
I have made a Micro assembler for programming the Microcode, we can write small programs using it.

## Slide 25: Example Microcode
Open the code.txt file and observe.
The macro keywords are always written in {} braces, they should not be changed. They represent Microcode decoder connections.
After that write your program using keyword that you defined in the braces.
Keyword1 Keyword2
represents data transfer from keyword 1 to keyword2
Keyword1 i Keyword2
represents immediate data taken as keyword to write to keyword2 register.
(some decimal or binary number) i Keyword2
    Represents immediate value to be written to keyword 2 address

## Slide 26: How to get hex file from the Microassembly Language ?
It can be assembled to binary by command
RDXasm <codefilename>.txt <hexfilename>
This will generate a <hexfilename>.RDXuasm
that you can open to see the hexcode.
We can test the program by command command
test <hexfilename>
Or I have made a programmer to programmer to program the ROM prog <hexfilename>
Then by pressing the button the microcode can be run.

## Slide 27: Limitations
There are a lot of limitations because of cost preferences, The aim had been to be make a realizable processor for self understanding and knowledge.
Vertical microcoding processor takes up a cycle for decoding time hence execution time. Vertical microcoding enables smaller databus width for ROM.
Data is fetched byte by byte for a 16 bit microinstruction to be executed, With an addition of 1 more ROM we can reduce fetch time to 1/3.

## Slide 28: Limitations
Microinstruction execution can be easily pipelined, for all of the 5 stages like.
  1. even data latch
  2. odd data fetch
  3. odd data latch
  4. execute
  5. even data fetch of next instruction
So we can possibly pipeline as
  5 1 2 3 4
  5 1 2 3 4
  5 1 2 3 4
  5 1 2 3 4
  Only colliding instruction are 5 and 2, such pipelining can be easily implemented by more complex sequencer

## Slide 29: Limitations
Due to Single bus architecture, It has no separate Bus control unit, hence there can not be pipelining at macro instruction level. (after the instruction set is defined in ROM).hence inherently slower than pipelined processor.
The ALU is insufficient, Example There is a Macro instruction set defined and has to be implemented, Here now even the addition of PC or IP takes a multicycle approach hence slow.

## Slide 30: Limitations
There is no internal hardware based stack for microcode jumps hence difficulty in managing recursion at microcode level, and hence difficulty in programming microcode for large instruction sets.
The processor Does not have any I/O right now, human interface not possible, There is also no interrupt hardware provision.
There is no halt instruction in the microcode.

## Slide 31: Future improvements to be implemented
Effeciency of Microcode fetching to be inproved by using 2 EEPROMs of 8 bit data width or 1 EEPROM of 16 bit Data width, Along with pipelining at microcode level to decrease CPI and hence increase effeciency.
Implementation of pipelining at microcode by redesigning microcode sequencer.
Provide ALU operations for addition and substraction, and extra registers for ALU based instruction set decoding.
Implement hardware based stack/queue/map for microcode jumps enabling to program complex instruction set decoding for emulation of large complex instruction sets like that of x86.
Provide Support for in System re programming of Control memory, by replacing ROM with a SRAM, that gets programmed by another primary control ROM during boot.

## Slide 32: Future improvements to be implemented
Provide I/O support for atleast 2 ports, 16x4 character based LED screen, for well known interfaces like I2C, SPI and USB.
Implement a small RISC instruction set to the microcode of processor, set up C compiler for it.
Implement BIOS routines, and a SD card support for the system.
Make provision for Cluster bus system, So that a by connecting multiple processors, Cluster computer can be made.

## Slide 33: Applications That this Final design promises
Cluster Computers.
Since the processor inherently uses multicycle approach, custered computer can provide a pipelineing support and parallel computing. Such clusters can be used as building blocks for super scalar Computers.
The processor provides provision for Programmable Control ROM hence instruction set emulation can be done.(Microcode of many presently available are either proprietary or in accessible by high level programmer)
Instruction set emulation can provide software Compatibility.